## Slide 1
WEARABLE BIOSENSORS
Continuous Health
Monitoring Patches
Real-Time Biosensing + Machine Learning
for Proactive Healthcare
TEAM NAME : CLEVER MIND
TEAM MEMBERS : Saranya.P
Thilagavathi.V
Yuvashree.B

## Slide 2
THE PROBLEM
Why current healthcare monitoring falls short
REACTIVE
Too Late
Lab tests detect problems AFTER they occur. Patients only check health when symptomatic — missing early-stage intervention windows.
INVASIVE
Painful & Inconvenient
Blood draws require clinic visits, cause discomfort, and provide only a single snapshot in time — not continuous data.
INCOMPLETE
Data Gaps
Smartwatches track steps but not biochemistry. No wearable currently monitors stress hormones, hydration, or metabolite levels accurately.

## Slide 3
WHAT ARE
HEALTH PATCHES?
Thin, flexible, skin-adherent devices with embedded biosensors that collect physiological data 24/7 — without drawing blood or requiring user interaction.
Work at molecular/chemical level
Non-invasive or minimally invasive
Stream real-time data continuously
Alert before symptoms appear
Biochemical
Detects glucose, cortisol, lactate at molecular level
Wireless
BLE / NFC data transmission to smartphone or gateway
Flexible
Polyimide & hydrogel substrates conform to skin naturally
AI-Powered
On-device ML inference for real-time anomaly detection

## Slide 4
KEY BIOMARKERS TRACKED
COMMERCIAL CASES
Blood Glucose
NORMAL RANGE
70–180 mg/dL
HOW DETECTED
Glucose oxidase enzyme reacts with glucose → electrical current ∝ concentration
USE CASES
Diabetes management, metabolic health, energy monitoring
KEY PLAYERS
Abbott FreeStyle Libre, Dexcom G7
EMERGING
Cortisol
NORMAL RANGE
10–25 nmol/L in sweat
HOW DETECTED
Electrochemical immunosensors or aptamer-based sensors detect cortisol in sweat
USE CASES
Stress monitoring, immune function, sleep quality, weight management
KEY PLAYERS
UC Berkeley & Stanford (research phase)
EARLY MARKET
Hydration
NORMAL RANGE
Na⁺: 10–100 mmol/L
HOW DETECTED
Ion-selective electrodes detect Na⁺, K⁺, Cl⁻ electrolytes in sweat
USE CASES
Athletic performance, elderly care, kidney & heart health monitoring
KEY PLAYERS
Epicore Biosystems, Gatorade GX

## Slide 5
HARDWARE ARCHITECTURE
INPUT
Biofluid Interface Layer
Hydrogel membrane collects sweat / interstitial fluid from skin
DETECT
Sensor Array
Electrochemical electrodes (Au, Pt) + optical (PPG) sensors
PROCESS
Signal Conditioning
Instrumentation amplifiers, ADC, noise filters (Savitzky-Golay)
COMPUTE
Microcontroller / SoC
ARM Cortex-M4, TinyML inference, power management IC
TRANSMIT
Wireless Module
Bluetooth Low Energy 5.0 (BLE) or NFC for data transmission
POWER
Flexible Power + Substrate
Biofuel cell or thin-film battery • Polyimide / PDMS base
▼
▼
▼
▼
▼
SKIN
CLOUD

## Slide 6
DATA TRAJECTORY
PATCH
(Sensor)
▶
Raw analog
signal (mV, μA)
EDGE MCU
(On-Patch)
▶
ADC, noise
filtering, BLE
SMARTPHONE
(Gateway)
▶
Feature extraction
anomaly flags
CLOUD ML
SERVER
▶
LSTM inference
trend analysis
DASHBOARD
/ ALERT
Clinician view
user notification
Electrochemical
Voltage & current readings from enzyme-based sensors — converted to concentration values via calibration ML
Optical (PPG)
Photoplethysmography for heart rate, SpO2, and blood volume pulse signals
Contextual
Accelerometer, skin temperature, ambient humidity — used as correction factors in ML models

## Slide 7
MACHINE LEARNING PIPELINE
5 stages from raw sensor signal to actionable health insight
01
Preprocessing
Baseline drift removal → Savitzky-Golay smoothing → Min-Max normalization
Python / SciPy
02
Calibration Model
Maps raw voltage/current to actual biomarker concentration (mg/dL, nmol/L)
Gradient Boosting / SVR
03
Anomaly Detection
Personalized Isolation Forest flags unusual glucose spikes, stress surges, dehydration
Isolation Forest
04
Predictive LSTM
Time-series forecasting predicts glucose/cortisol levels 30–60 minutes ahead
LSTM / Transformer
05
Federated Learning
Devices train locally; only weight updates shared to cloud — never raw health data
TensorFlow Federated

## Slide 8
ML MODELS IN DEPTH
ANOMALY DETECTION
from sklearn.ensemble import IsolationForest detector = IsolationForest( contamination=0.05, n_estimators=100 ) detector.fit(normal_data) # Real-time inference score = detector.score_samples( [new_reading])[0] alert = score < -0.3
LSTM PREDICTOR
model = Sequential([ LSTM(128, return_sequences=True, input_shape=(60, 4)), Dropout(0.2), LSTM(64), Dropout(0.2), Dense(32, activation='relu'), Dense(30) # 30min ahead ]) model.compile( loss='huber')

## Slide 9
REAL-TIME DEPLOYMENT STACK
TIER 1
On-Patch Edge
TensorFlow Lite Micro • ARM Cortex-M4 • BLE 5.0
Noise filtering, basic anomaly scoring, signal compression
▼
TIER 2
Mobile App (iOS / Android)
CoreML (iOS) • ONNX Runtime (Android) • React Native
Real-time dashboard, on-device LSTM inference, push notifications
▼
TIER 3
Cloud Backend
FastAPI + Docker + Kubernetes • MLflow • Airflow • AWS HealthLake
Model retraining, federated aggregation, FHIR integration, HIPAA storage
▼
TIER 4
Clinician Portal
React Dashboard • D3.js • HL7 FHIR API
Population-level views, alert triage, prescription triggers, EHR sync

## Slide 10
CHALLENGES & SOLUTIONS AS PER OUR IDEOLOGY
⚠ CHALLENGE
Sweat composition varies with activity level
✓ SOLUTION
Multivariate correction models using temperature, pH, and flow rate as co-sensors
⚠ CHALLENGE
Sensor drift over time reduces accuracy
✓ SOLUTION
Automatic recalibration algorithms triggered by reference models or scheduled lab checks
⚠ CHALLENGE
High individual variability between users
✓ SOLUTION
Personalized fine-tuning via transfer learning from a pre-trained global model
⚠ CHALLENGE
Battery life severely limited on flexible form factor
✓ SOLUTION
Biofuel cells (powered by sweat glucose) + NFC energy harvesting for passive operation
⚠ CHALLENGE
FDA regulatory approval is slow and costly
✓ SOLUTION
510(k) De Novo pathway using established predicates; predicate matching from existing CGMs
⚠ CHALLENGE
Raw health data privacy and security concerns
✓ SOLUTION
Federated learning keeps data on-device; AES-256 encryption; HIPAA-compliant cloud storage

## Slide 11
MARKET LANDSCAPE & ROADMAP
$62B
CGM market by 2030
422M
Diabetics globally needing monitoring
$300B
Annual cost of workplace stress (US)
28%
CAGR of wearable biosensor market
PHASE 1 · 0–6 months
Research & Prototype
Pick 1 biomarker • Build sensor MCU prototype • Collect labeled dataset
PHASE 2 · 6–18 months
Clinical Validation
IRB trial (50–200 subjects) • Compare to gold-standard lab tests • Train ML pipeline
PHASE 3 · 18–36 months
Regulatory & Mfg
FDA 510(k) / De Novo submission • CE Mark (Europe) • Scale manufacturing
PHASE 4 · 36+ months
Commercial Launch
B2C direct • B2B hospital SaaS • Subscription analytics platform

## Slide 12
KEY TAKEAWAYS
The Future of Proactive Healthcare
01
Biochemistry + AI = Breakthrough
Combining electrochemical sensors with ML unlocks real-time insights never possible with traditional diagnostics.
02
Prevention Over Treatment
Predictive LSTM models can warn users 30–60 minutes before critical biomarker events, enabling proactive action.
03
Privacy-First Architecture
Federated learning ensures powerful population-level AI improvements without ever exposing raw patient data.
04
Biggest Opportunity: Cortisol
Stress monitoring has a massive market with almost no wearable solutions — whoever solves it first wins big.